## Slide 1
Chapter 4 Network Layer
Computer Networking: A Top Down Approach 6th edition Jim Kurose, Keith Ross Addison-Wesley March 2012
A note on the use of these ppt slides:
We’re making these slides freely available to all (faculty, students, readers). They’re in PowerPoint form so you see the animations; and can add, modify, and delete slides (including this one) and slide content to suit your needs. They obviously represent a lot of work on our part. In return for use, we only ask the following:
If you use these slides (e.g., in a class) that you mention their source (after all, we’d like people to use our book!)
If you post any slides on a www site, that you note that they are adapted from (or perhaps identical to) our slides, and note our copyright of this material.
Thanks and enjoy! JFK/KWR
All material copyright 1996-2012
J.F Kurose and K.W. Ross, All Rights Reserved

## Slide 2: Chapter 4: network layer
chapter goals:
understand principles behind network layer services:
  network layer service models
  forwarding versus routing
  how a router works
  routing (path selection)
  broadcast, multicast
instantiation, implementation in the Internet

## Slide 3
4.1 introduction
4.2 virtual circuit and datagram networks
4.3 what’s inside a router
4.4 IP: Internet Protocol
  datagram format
  IPv4 addressing
  ICMP
  IPv6
4.5 routing algorithms
  link state
  distance vector
  hierarchical routing
4.6 routing in the Internet
  RIP
  OSPF
  BGP
4.7 broadcast and multicast routing
Chapter 4: outline

## Slide 4: Network layer
transport segment from sending to receiving host
on sending side encapsulates segments into datagrams
on receiving side, delivers segments to transport layer
network layer protocols in every host, router
router examines header fields in all IP datagrams passing through it
application
transport
network
data link
physical
application
transport
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical

## Slide 5: Two key network-layer functions
forwarding: move packets from router’s input to appropriate router output
routing: determine route taken by packets from source to dest.
  routing algorithms
analogy:
routing: process of planning trip from source to dest
forwarding: process of getting through single interchange

## Slide 6
1
2
3
0111
value in arriving
packet’s header
routing algorithm
local forwarding table
header value
output link
0100
0101
0111
1001
3
2
2
1
Interplay between routing and forwarding
routing algorithm determines
end-end-path through network
forwarding table determines
local forwarding at this router

## Slide 7: Connection setup
3rd important function in some network architectures:
  ATM, frame relay, X.25
before datagrams flow, two end hosts and intervening routers establish virtual connection
  routers get involved
network vs transport layer connection service:
  network: between two hosts (may also involve intervening routers in case of VCs)
  transport: between two processes

## Slide 8: Network service model
Q: What service model for “channel” transporting datagrams from sender to receiver?
example services for individual datagrams:
guaranteed delivery
guaranteed delivery with less than 40 msec delay
example services for a flow of datagrams:
in-order datagram delivery
guaranteed minimum bandwidth to flow
restrictions on changes in inter-packet spacing

## Slide 9: Network layer service models:
Network
Architecture
Internet
ATM
ATM
ATM
ATM
Service
Model
best effort
CBR
VBR
ABR
UBR
Bandwidth
none
constant
rate
guaranteed
rate
guaranteed
minimum
none
Loss
no
yes
yes
no
no
Order
no
yes
yes
yes
yes
Timing
no
yes
yes
no
no
Congestion
feedback
no (inferred
via loss)
no
congestion
no
congestion
yes
no
Guarantees ?

## Slide 10
4.1 introduction
4.2 virtual circuit and datagram networks
4.3 what’s inside a router
4.4 IP: Internet Protocol
  datagram format
  IPv4 addressing
  ICMP
  IPv6
4.5 routing algorithms
  link state
  distance vector
  hierarchical routing
4.6 routing in the Internet
  RIP
  OSPF
  BGP
4.7 broadcast and multicast routing
Chapter 4: outline

## Slide 11: Connection, connection-less service
datagram network provides network-layer connectionless service
virtual-circuit network provides network-layer connection service
analogous to TCP/UDP connecton-oriented / connectionless transport-layer services, but:
  service: host-to-host
  no choice: network provides one or the other
  implementation: in network core

## Slide 12: Virtual circuits
call setup, teardown for each call before data can flow
each packet carries VC identifier (not destination host address)
every router on source-dest path maintains “state” for each passing connection
link, router resources (bandwidth, buffers) may be allocated to VC (dedicated resources = predictable service)
“source-to-dest path behaves much like telephone circuit”
  performance-wise
  network actions along source-to-dest path

## Slide 13: VC implementation
a VC consists of:
  path from source to destination
  VC numbers, one number for each link along path
  entries in forwarding tables in routers along path
packet belonging to VC carries VC number (rather than dest address)
VC number can be changed on each link.
  new VC number comes from forwarding table

## Slide 14: VC forwarding table
12
22
32
1
2
3
VC number
interface
number
Incoming interface Incoming VC # Outgoing interface Outgoing VC #
1 12 3 22
2 63 1 18
3 7 2 17
1 97 3 87
… … … …
forwarding table in
northwest router:
VC routers maintain connection state information!

## Slide 15: Virtual circuits: signaling protocols
application
transport
network
data link
physical
used to setup, maintain teardown VC
used in ATM, frame-relay, X.25
not used in today’s Internet
1. initiate call
2. incoming call
3. accept call
4. call connected
5. data flow begins
6. receive data
application
transport
network
data link
physical

## Slide 16: Datagram networks
no call setup at network layer
routers: no state about end-to-end connections
  no network-level concept of “connection”
packets forwarded using destination host address
1. send datagrams
application
transport
network
data link
physical
application
transport
network
data link
physical
2. receive datagrams

## Slide 17: Datagram forwarding table
1
2
3
IP destination address in
arriving packet’s header
routing algorithm
local forwarding table
dest address
output link
address-range 1
address-range 2
address-range 3
address-range 4
3
2
2
1
4 billion IP addresses, so rather than list individual destination address
list range of addresses
(aggregate table entries)

## Slide 18: Datagram forwarding table
Destination Address Range
11001000 00010111 00010000 00000000
through
11001000 00010111 00010111 11111111
11001000 00010111 00011000 00000000
through
11001000 00010111 00011000 11111111
11001000 00010111 00011001 00000000
through
11001000 00010111 00011111 11111111
otherwise
Link Interface
0
1
2
3
Q: but what happens if ranges don’t divide up so nicely?

## Slide 19: Longest prefix matching
Destination Address Range
11001000 00010111 00010*** *********
11001000 00010111 00011000 *********
11001000 00010111 00011*** *********
otherwise
DA: 11001000 00010111 00011000 10101010
examples:
DA: 11001000 00010111 00010110 10100001
which interface?
which interface?
when looking for forwarding table entry for given destination address, use longest address prefix that matches destination address.
longest prefix matching
Link interface
0
1
2
3

## Slide 20: Datagram or VC network: why?
Internet (datagram)
data exchange among computers
  “elastic” service, no strict timing req.
many link types
  different characteristics
  uniform service difficult
“smart” end systems (computers)
  can adapt, perform control, error recovery
  simple inside network, complexity at “edge”
ATM (VC)
evolved from telephony
human conversation:
  strict timing, reliability requirements
  need for guaranteed service
“dumb” end systems
  telephones
  complexity inside network

## Slide 21
4.1 introduction
4.2 virtual circuit and datagram networks
4.3 what’s inside a router
4.4 IP: Internet Protocol
  datagram format
  IPv4 addressing
  ICMP
  IPv6
4.5 routing algorithms
  link state
  distance vector
  hierarchical routing
4.6 routing in the Internet
  RIP
  OSPF
  BGP
4.7 broadcast and multicast routing
Chapter 4: outline

## Slide 22: Router architecture overview
two key router functions:
run routing algorithms/protocol (RIP, OSPF, BGP)
forwarding datagrams from incoming to outgoing link
high-seed
switching
fabric
routing
processor
router input ports
router output ports
forwarding data plane (hardware)
routing, management
control plane (software)
forwarding tables computed,
pushed to input ports

## Slide 23: Input port functions
line
termination
link
layer
protocol
(receive)
lookup,
forwarding
queueing
decentralized switching:
given datagram dest., lookup output port using forwarding table in input port memory (“match plus action”)
goal: complete input port processing at ‘line speed’
queuing: if datagrams arrive faster than forwarding rate into switch fabric
physical layer:
bit-level reception
data link layer:
e.g., Ethernet
see chapter 5
switch
fabric

## Slide 24: Switching fabrics
transfer packet from input buffer to appropriate output buffer
switching rate: rate at which packets can be transfer from inputs to outputs
  often measured as multiple of input/output line rate
  N inputs: switching rate N times line rate desirable
three types of switching fabrics
memory
memory
bus
crossbar

## Slide 25: Switching via memory
first generation routers:
traditional computers with switching under direct control of CPU
packet copied to system’s memory
speed limited by memory bandwidth (2 bus crossings per datagram)
input
port
(e.g.,
Ethernet)
memory
output
port
(e.g.,
Ethernet)
system bus

## Slide 26: Switching via a bus
datagram from input port memory
to output port memory via a shared bus
bus contention: switching speed limited by bus bandwidth
32 Gbps bus, Cisco 5600: sufficient speed for access and enterprise routers
bus

## Slide 27: Switching via interconnection network
overcome bus bandwidth limitations
banyan networks, crossbar, other interconnection nets initially developed to connect processors in multiprocessor
advanced design: fragmenting datagram into fixed length cells, switch cells through the fabric.
Cisco 12000: switches 60 Gbps through the interconnection network
crossbar

## Slide 28: Output ports
buffering required when datagrams arrive from fabric faster than the transmission rate
scheduling discipline chooses among queued datagrams for transmission
line
termination
link
layer
protocol
(send)
switch
fabric
datagram
buffer
queueing

## Slide 29: Output port queueing
buffering when arrival rate via switch exceeds output line speed
queueing (delay) and loss due to output port buffer overflow!
at t, packets more
from input to output
one packet time later
switch
fabric
switch
fabric

## Slide 30: How much buffering?
RFC 3439 rule of thumb: average buffering equal to “typical” RTT (say 250 msec) times link capacity C
  e.g., C = 10 Gpbs link: 2.5 Gbit buffer
recent recommendation: with N flows, buffering equal to
RTT C
.
N

## Slide 31: Input port queuing
fabric slower than input ports combined -> queueing may occur at input queues
  queueing delay and loss due to input buffer overflow!
Head-of-the-Line (HOL) blocking: queued datagram at front of queue prevents others in queue from moving forward
output port contention:
only one red datagram can be transferred. lower red packet is blocked
switch
fabric
one packet time later: green packet experiences HOL blocking
switch
fabric

## Slide 32
4.1 introduction
4.2 virtual circuit and datagram networks
4.3 what’s inside a router
4.4 IP: Internet Protocol
  datagram format
  IPv4 addressing
  ICMP
  IPv6
4.5 routing algorithms
  link state
  distance vector
  hierarchical routing
4.6 routing in the Internet
  RIP
  OSPF
  BGP
4.7 broadcast and multicast routing
Chapter 4: outline

## Slide 33: The Internet network layer
forwarding
table
host, router network layer functions:
routing protocols
path selection
RIP, OSPF, BGP
IP protocol
addressing conventions
datagram format
packet handling conventions
ICMP protocol
error reporting
router “signaling”
transport layer: TCP, UDP
link layer
physical layer
network
layer

## Slide 34: IP datagram format
ver
length
32 bits
data
(variable length,
typically a TCP
or UDP segment)
16-bit identifier
header
checksum
time to
live
32 bit source IP address
head.
len
type of
service
flgs
fragment
offset
upper
layer
32 bit destination IP address
options (if any)
IP protocol version
number
header length
(bytes)
upper layer protocol
to deliver payload to
total datagram
length (bytes)
“type” of data
for
fragmentation/
reassembly
max number
remaining hops
(decremented at
each router)
e.g. timestamp,
record route
taken, specify
list of routers
to visit.
how much overhead?
20 bytes of TCP
20 bytes of IP
= 40 bytes + app layer overhead

## Slide 35: IP fragmentation, reassembly
network links have MTU (max.transfer size) - largest possible link-level frame
  different link types, different MTUs
large IP datagram divided (“fragmented”) within net
  one datagram becomes several datagrams
  “reassembled” only at final destination
  IP header bits used to identify, order related fragments
fragmentation:
in: one large datagram
out: 3 smaller datagrams
reassembly
…
…

## Slide 36: IP fragmentation, reassembly
ID
=x
offset
=0
fragflag
=0
length
=4000
ID
=x
offset
=0
fragflag
=1
length
=1500
ID
=x
offset
=185
fragflag
=1
length
=1500
ID
=x
offset
=370
fragflag
=0
length
=1040
one large datagram becomes
several smaller datagrams
example:
4000 byte datagram
MTU = 1500 bytes
1480 bytes in data field
offset =
1480/8

## Slide 37
4.1 introduction
4.2 virtual circuit and datagram networks
4.3 what’s inside a router
4.4 IP: Internet Protocol
  datagram format
  IPv4 addressing
  ICMP
  IPv6
4.5 routing algorithms
  link state
  distance vector
  hierarchical routing
4.6 routing in the Internet
  RIP
  OSPF
  BGP
4.7 broadcast and multicast routing
Chapter 4: outline

## Slide 38: IP addressing: introduction
IP address: 32-bit identifier for host, router interface
interface: connection between host/router and physical link
  router’s typically have multiple interfaces
  host typically has one or two interfaces (e.g., wired Ethernet, wireless 802.11)
IP addresses associated with each interface
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.1 = 11011111 00000001 00000001 00000001
223
1
1
1

## Slide 39: IP addressing: introduction
Q: how are interfaces actually connected?
A: we’ll learn about that in chapter 5, 6.
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
A: wired Ethernet interfaces connected by Ethernet switches
A: wireless WiFi interfaces connected by WiFi base station
For now: don’t need to worry about how one interface is connected to another (with no intervening router)

## Slide 40: Subnets
IP address:
  subnet part - high order bits
  host part - low order bits
what’s a subnet ?
  device interfaces with same subnet part of IP address
  can physically reach each other without intervening router
network consisting of 3 subnets
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.9
223.1.3.2
223.1.3.1
subnet
223.1.1.2
223.1.3.27
223.1.2.2
223.1.2.1

## Slide 41: Subnets
recipe
to determine the subnets, detach each interface from its host or router, creating islands of isolated networks
each isolated network is called a subnet
subnet mask: /24
223.1.1.0/24
223.1.2.0/24
223.1.3.0/24
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.9
223.1.3.2
223.1.3.1
subnet
223.1.1.2
223.1.3.27
223.1.2.2
223.1.2.1

## Slide 42: Subnets
how many?
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.2
223.1.2.1
223.1.2.6
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.2
223.1.7.0
223.1.7.1
223.1.8.0
223.1.8.1
223.1.9.1
223.1.9.2

## Slide 43: IP addressing: CIDR
CIDR: Classless InterDomain Routing
  subnet portion of address of arbitrary length
  address format: a.b.c.d/x, where x is # bits in subnet portion of address
11001000 00010111 00010000 00000000
subnet
part
host
part
200.23.16.0/23

## Slide 44: IP addresses: how to get one?
Q: How does a host get IP address?
hard-coded by system admin in a file
  Windows: control-panel->network->configuration->tcp/ip->properties
  UNIX: /etc/rc.config
DHCP: Dynamic Host Configuration Protocol: dynamically get address from as server
  “plug-and-play”

## Slide 45: DHCP: Dynamic Host Configuration Protocol
goal: allow host to dynamically obtain its IP address from network server when it joins network
  can renew its lease on address in use
  allows reuse of addresses (only hold address while connected/“on”)
  support for mobile users who want to join network (more shortly)
DHCP overview:
  host broadcasts “DHCP discover” msg [optional]
  DHCP server responds with “DHCP offer” msg [optional]
  host requests IP address: “DHCP request” msg
  DHCP server sends address: “DHCP ack” msg

## Slide 46: DHCP client-server scenario
223.1.1.0/24
223.1.2.0/24
223.1.3.0/24
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.9
223.1.3.2
223.1.3.1
223.1.1.2
223.1.3.27
223.1.2.2
223.1.2.1
DHCP
server
arriving DHCP
client needs
address in this
network

## Slide 47: DHCP client-server scenario
DHCP server: 223.1.2.5
arriving
client
DHCP discover
src : 0.0.0.0, 68
dest.: 255.255.255.255,67
yiaddr: 0.0.0.0
transaction ID: 654
DHCP offer
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 654
lifetime: 3600 secs
DHCP request
src: 0.0.0.0, 68
dest:: 255.255.255.255, 67
yiaddrr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs
DHCP ACK
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs

## Slide 48: DHCP: more than IP addresses
DHCP can return more than just allocated IP address on subnet:
  address of first-hop router for client
  name and IP address of DNS sever
  network mask (indicating network versus host portion of address)

## Slide 49: DHCP: example
connecting laptop needs its IP address, addr of first-hop router, addr of DNS server: use DHCP
router with DHCP
server built into
router
DHCP request encapsulated in UDP, encapsulated in IP, encapsulated in 802.1 Ethernet
Ethernet frame broadcast (dest: FFFFFFFFFFFF) on LAN, received at router running DHCP server
Ethernet demuxed to IP demuxed, UDP demuxed to DHCP
168.1.1.1
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP

## Slide 50: DHCP: example
DCP server formulates DHCP ACK containing client’s IP address, IP address of first-hop router for client, name & IP address of DNS server
encapsulation of DHCP server, frame forwarded to client, demuxing up to DHCP at client
router with DHCP
server built into
router
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
client now knows its IP address, name and IP address of DSN server, IP address of its first-hop router

## Slide 51: DHCP: Wireshark output (home LAN)
Message type: Boot Reply (2)
Hardware type: Ethernet
Hardware address length: 6
Hops: 0
Transaction ID: 0x6b3a11b7
Seconds elapsed: 0
Bootp flags: 0x0000 (Unicast)
Client IP address: 192.168.1.101 (192.168.1.101)
Your (client) IP address: 0.0.0.0 (0.0.0.0)
Next server IP address: 192.168.1.1 (192.168.1.1)
Relay agent IP address: 0.0.0.0 (0.0.0.0)
Client MAC address: Wistron_23:68:8a (00:16:d3:23:68:8a)
Server host name not given
Boot file name not given
Magic cookie: (OK)
Option: (t=53,l=1) DHCP Message Type = DHCP ACK
Option: (t=54,l=4) Server Identifier = 192.168.1.1
Option: (t=1,l=4) Subnet Mask = 255.255.255.0
Option: (t=3,l=4) Router = 192.168.1.1
Option: (6) Domain Name Server
Length: 12; Value: 445747E2445749F244574092;
IP Address: 68.87.71.226;
IP Address: 68.87.73.242;
IP Address: 68.87.64.146
Option: (t=15,l=20) Domain Name = "hsd1.ma.comcast.net."
reply
Message type: Boot Request (1)
Hardware type: Ethernet
Hardware address length: 6
Hops: 0
Transaction ID: 0x6b3a11b7
Seconds elapsed: 0
Bootp flags: 0x0000 (Unicast)
Client IP address: 0.0.0.0 (0.0.0.0)
Your (client) IP address: 0.0.0.0 (0.0.0.0)
Next server IP address: 0.0.0.0 (0.0.0.0)
Relay agent IP address: 0.0.0.0 (0.0.0.0)
Client MAC address: Wistron_23:68:8a (00:16:d3:23:68:8a)
Server host name not given
Boot file name not given
Magic cookie: (OK)
Option: (t=53,l=1) DHCP Message Type = DHCP Request
Option: (61) Client identifier
Length: 7; Value: 010016D323688A;
Hardware type: Ethernet
Client MAC address: Wistron_23:68:8a (00:16:d3:23:68:8a)
Option: (t=50,l=4) Requested IP Address = 192.168.1.101
Option: (t=12,l=5) Host Name = "nomad"
Option: (55) Parameter Request List
Length: 11; Value: 010F03062C2E2F1F21F92B
1 = Subnet Mask; 15 = Domain Name
3 = Router; 6 = Domain Name Server
44 = NetBIOS over TCP/IP Name Server
……
request

## Slide 52: IP addresses: how to get one?
Q: how does network get subnet part of IP addr?
A: gets allocated portion of its provider ISP’s address space
ISP's block 11001000 00010111 00010000 00000000 200.23.16.0/20
Organization 0 11001000 00010111 00010000 00000000 200.23.16.0/23
Organization 1 11001000 00010111 00010010 00000000 200.23.18.0/23
Organization 2 11001000 00010111 00010100 00000000 200.23.20.0/23
... ….. …. ….
Organization 7 11001000 00010111 00011110 00000000 200.23.30.0/23

## Slide 53: Hierarchical addressing: route aggregation
“Send me anything
with addresses
beginning
200.23.16.0/20”
200.23.16.0/23
200.23.18.0/23
200.23.30.0/23
Fly-By-Night-ISP
Organization 0
Organization 7
Internet
Organization 1
ISPs-R-Us
“Send me anything
with addresses
beginning
199.31.0.0/16”
200.23.20.0/23
Organization 2
.
.
.
.
.
.
hierarchical addressing allows efficient advertisement of routing
information:

## Slide 54: Hierarchical addressing: more specific routes
ISPs-R-Us has a more specific route to Organization 1
“Send me anything
with addresses
beginning
200.23.16.0/20”
200.23.16.0/23
200.23.18.0/23
200.23.30.0/23
Fly-By-Night-ISP
Organization 0
Organization 7
Internet
Organization 1
ISPs-R-Us
“Send me anything
with addresses
beginning 199.31.0.0/16
or 200.23.18.0/23”
200.23.20.0/23
Organization 2
.
.
.
.
.
.

## Slide 55: IP addressing: the last word...
Q: how does an ISP get block of addresses?
A: ICANN: Internet Corporation for Assigned
Names and Numbers http://www.icann.org/
  allocates addresses
  manages DNS
  assigns domain names, resolves disputes

## Slide 56: NAT: network address translation
10.0.0.1
10.0.0.2
10.0.0.3
10.0.0.4
138.76.29.7
local network
(e.g., home network)
10.0.0/24
rest of
Internet
datagrams with source or
destination in this network
have 10.0.0/24 address for
source, destination (as usual)
all datagrams leaving local
network have same single source NAT IP address: 138.76.29.7,different source port numbers

## Slide 57: NAT: network address translation
motivation: local network uses just one IP address as far as outside world is concerned:
  range of addresses not needed from ISP: just one IP address for all devices
  can change addresses of devices in local network without notifying outside world
  can change ISP without changing addresses of devices in local network
  devices inside local net not explicitly addressable, visible by outside world (a security plus)

## Slide 58: NAT: network address translation
implementation: NAT router must:
  outgoing datagrams: replace (source IP address, port #) of every outgoing datagram to (NAT IP address, new port #)
    . . . remote clients/servers will respond using (NAT IP address, new port #) as destination addr
  remember (in NAT translation table) every (source IP address, port #) to (NAT IP address, new port #) translation pair
  incoming datagrams: replace (NAT IP address, new port #) in dest fields of every incoming datagram with corresponding (source IP address, port #) stored in NAT table

## Slide 59: NAT: network address translation
10.0.0.1
10.0.0.2
10.0.0.3
S: 10.0.0.1, 3345
D: 128.119.40.186, 80
1
10.0.0.4
138.76.29.7
1: host 10.0.0.1
sends datagram to
128.119.40.186, 80
NAT translation table
WAN side addr LAN side addr
138.76.29.7, 5001 10.0.0.1, 3345
…… ……
S: 128.119.40.186, 80
D: 10.0.0.1, 3345
4
S: 138.76.29.7, 5001
D: 128.119.40.186, 80
2
2: NAT router
changes datagram
source addr from
10.0.0.1, 3345 to
138.76.29.7, 5001,
updates table
S: 128.119.40.186, 80
D: 138.76.29.7, 5001
3
3: reply arrives
dest. address:
138.76.29.7, 5001
4: NAT router
changes datagram
dest addr from
138.76.29.7, 5001 to 10.0.0.1, 3345

## Slide 60: NAT: network address translation
16-bit port-number field:
  60,000 simultaneous connections with a single LAN-side address!
NAT is controversial:
  routers should only process up to layer 3
  violates end-to-end argument
    NAT possibility must be taken into account by app designers, e.g., P2P applications
  address shortage should instead be solved by IPv6

## Slide 61: NAT traversal problem
client wants to connect to server with address 10.0.0.1
  server address 10.0.0.1 local to LAN (client can’t use it as destination addr)
  only one externally visible NATed address: 138.76.29.7
solution1: statically configure NAT to forward incoming connection requests at given port to server
  e.g., (123.76.29.7, port 2500) always forwarded to 10.0.0.1 port 25000
10.0.0.1
10.0.0.4
NAT
router
138.76.29.7
client
?

## Slide 62: NAT traversal problem
solution 2: Universal Plug and Play (UPnP) Internet Gateway Device (IGD) Protocol. Allows NATed host to:
  learn public IP address (138.76.29.7)
  add/remove port mappings (with lease times)
  i.e., automate static NAT port map configuration
10.0.0.1
NAT
router
IGD

## Slide 63: NAT traversal problem
solution 3: relaying (used in Skype)
  NATed client establishes connection to relay
  external client connects to relay
  relay bridges packets between to connections
138.76.29.7
client
1. connection to
relay initiated
by NATed host
2. connection to
relay initiated
by client
3. relaying
established
NAT
router
10.0.0.1

## Slide 64
4.1 introduction
4.2 virtual circuit and datagram networks
4.3 what’s inside a router
4.4 IP: Internet Protocol
  datagram format
  IPv4 addressing
  ICMP
  IPv6
4.5 routing algorithms
  link state
  distance vector
  hierarchical routing
4.6 routing in the Internet
  RIP
  OSPF
  BGP
4.7 broadcast and multicast routing
Chapter 4: outline

## Slide 65: ICMP: internet control message protocol
used by hosts & routers to communicate network-level information
  error reporting: unreachable host, network, port, protocol
  echo request/reply (used by ping)
network-layer “above” IP:
  ICMP msgs carried in IP datagrams
ICMP message: type, code plus first 8 bytes of IP datagram causing error
Type Code description
0 0 echo reply (ping)
3 0 dest. network unreachable
3 1 dest host unreachable
3 2 dest protocol unreachable
3 3 dest port unreachable
3 6 dest network unknown
3 7 dest host unknown
4 0 source quench (congestion
control - not used)
8 0 echo request (ping)
9 0 route advertisement
10 0 router discovery
11 0 TTL expired
12 0 bad IP header

## Slide 66: Traceroute and ICMP
source sends series of UDP segments to dest
  first set has TTL =1
  second set has TTL=2, etc.
  unlikely port number
when nth set of datagrams arrives to nth router:
  router discards datagrams
  and sends source ICMP messages (type 11, code 0)
  ICMP messages includes name of router & IP address
when ICMP messages arrives, source records RTTs
stopping criteria:
UDP segment eventually arrives at destination host
destination returns ICMP “port unreachable” message (type 3, code 3)
source stops
3 probes
3 probes
3 probes

## Slide 67: IPv6: motivation
initial motivation: 32-bit address space soon to be completely allocated.
additional motivation:
  header format helps speed processing/forwarding
  header changes to facilitate QoS
IPv6 datagram format:
  fixed-length 40 byte header
  no fragmentation allowed

## Slide 68: IPv6 datagram format
priority: identify priority among datagrams in flow
flow Label: identify datagrams in same “flow.”
(concept of“flow” not well defined).
next header: identify upper layer protocol for data
data
destination address
(128 bits)
source address
(128 bits)
payload len
next hdr
hop limit
flow label
pri
ver
32 bits

## Slide 69: Other changes from IPv4
checksum: removed entirely to reduce processing time at each hop
options: allowed, but outside of header, indicated by “Next Header” field
ICMPv6: new version of ICMP
  additional message types, e.g. “Packet Too Big”
  multicast group management functions

## Slide 70: Transition from IPv4 to IPv6
not all routers can be upgraded simultaneously
  no “flag days”
  how will network operate with mixed IPv4 and IPv6 routers?
tunneling: IPv6 datagram carried as payload in IPv4 datagram among IPv4 routers
IPv4 source, dest addr
IPv4 header fields
IPv4 datagram
IPv6 datagram
IPv4 payload
UDP/TCP payload
IPv6 source dest addr
IPv6 header fields

## Slide 71: Tunneling
physical view:
IPv4
IPv4
A
B
IPv6
IPv6
E
IPv6
IPv6
F
C
D
logical view:
IPv4 tunnel
connecting IPv6 routers
E
IPv6
IPv6
F
A
B
IPv6
IPv6

## Slide 72: Tunneling
flow: X
src: A
dest: F
data
A-to-B:
IPv6
Flow: X
Src: A
Dest: F
data
src:B
dest: E
B-to-C:
IPv6 inside
IPv4
E-to-F:
IPv6
flow: X
src: A
dest: F
data
B-to-C:
IPv6 inside
IPv4
Flow: X
Src: A
Dest: F
data
src:B
dest: E
physical view:
A
B
IPv6
IPv6
E
IPv6
IPv6
F
C
D
logical view:
IPv4 tunnel
connecting IPv6 routers
E
IPv6
IPv6
F
A
B
IPv6
IPv6
IPv4
IPv4

## Slide 73
4.1 introduction
4.2 virtual circuit and datagram networks
4.3 what’s inside a router
4.4 IP: Internet Protocol
  datagram format
  IPv4 addressing
  ICMP
  IPv6
4.5 routing algorithms
  link state
  distance vector
  hierarchical routing
4.6 routing in the Internet
  RIP
  OSPF
  BGP
4.7 broadcast and multicast routing
Chapter 4: outline

## Slide 74: Interplay between routing, forwarding
1
2
3
IP destination address in
arriving packet’s header
routing algorithm
local forwarding table
dest address
output link
address-range 1
address-range 2
address-range 3
address-range 4
3
2
2
1
routing algorithm determines
end-end-path through network
forwarding table determines
local forwarding at this router

## Slide 75: Graph abstraction
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
graph: G = (N,E)
N = set of routers = { u, v, w, x, y, z }
E = set of links ={ (u,v), (u,x), (v,x), (v,w), (x,w), (x,y), (w,y), (w,z), (y,z) }
aside: graph abstraction is useful in other network contexts, e.g.,
P2P, where N is set of peers and E is set of TCP connections

## Slide 76: Graph abstraction: costs
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
c(x,x’) = cost of link (x,x’)
e.g., c(w,z) = 5
cost could always be 1, or
inversely related to bandwidth,
or inversely related to
congestion
cost of path (x1, x2, x3,…, xp) = c(x1,x2) + c(x2,x3) + … + c(xp-1,xp)
key question: what is the least-cost path between u and z ?
routing algorithm: algorithm that finds that least cost path

## Slide 77: Routing algorithm classification
Q: global or decentralized information?
global:
all routers have complete topology, link cost info
“link state” algorithms
decentralized:
router knows physically-connected neighbors, link costs to neighbors
iterative process of computation, exchange of info with neighbors
“distance vector” algorithms
Q: static or dynamic?
static:
routes change slowly over time
dynamic:
routes change more quickly
  periodic update
  in response to link cost changes

## Slide 78
4.1 introduction
4.2 virtual circuit and datagram networks
4.3 what’s inside a router
4.4 IP: Internet Protocol
  datagram format
  IPv4 addressing
  ICMP
  IPv6
4.5 routing algorithms
  link state
  distance vector
  hierarchical routing
4.6 routing in the Internet
  RIP
  OSPF
  BGP
4.7 broadcast and multicast routing
Chapter 4: outline

## Slide 79: A Link-State Routing Algorithm
Dijkstra’s algorithm
net topology, link costs known to all nodes
  accomplished via “link state broadcast”
  all nodes have same info
computes least cost paths from one node (‘source”) to all other nodes
  gives forwarding table for that node
iterative: after k iterations, know least cost path to k dest.’s
notation:
c(x,y): link cost from node x to y; = ∞ if not direct neighbors
D(v): current value of cost of path from source to dest. v
p(v): predecessor node along path from source to v
N': set of nodes whose least cost path definitively known

## Slide 80: Dijsktra’s Algorithm
1 Initialization:
2 N' = {u}
3 for all nodes v
4 if v adjacent to u
5 then D(v) = c(u,v)
6 else D(v) = ∞
7
8 Loop
9 find w not in N' such that D(w) is a minimum
10 add w to N'
11 update D(v) for all v adjacent to w and not in N' :
12 D(v) = min( D(v), D(w) + c(w,v) )
13 /* new cost to v is either old cost to v or known
14 shortest path cost to w plus cost from w to v */
15 until all nodes in N'

## Slide 81
w
3
4
v
x
u
5
3
7
4
y
8
z
2
7
9
Dijkstra’s algorithm: example
Step
N'
D(v)
p(v)
0
1
2
3
4
5
D(w)
p(w)
D(x)
p(x)
D(y)
p(y)
D(z)
p(z)
u
∞
∞
7,u
3,u
5,u
uw
∞
11,w
6,w
5,u
14,x
11,w
6,w
uwx
uwxv
14,x
10,v
uwxvy
12,y
notes:
construct shortest path tree by tracing predecessor nodes
ties can exist (can be broken arbitrarily)
uwxvyz

## Slide 82: Dijkstra’s algorithm: another example
Step
0
1
2
3
4
5
N'
u
ux
uxy
uxyv
uxyvw
uxyvwz
D(v),p(v)
2,u
2,u
2,u
D(w),p(w)
5,u
4,x
3,y
3,y
D(x),p(x)
1,u
D(y),p(y)
∞
2,x
D(z),p(z)
∞
∞
4,y
4,y
4,y
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5

## Slide 83: Dijkstra’s algorithm: example (2)
u
y
x
w
v
z
resulting shortest-path tree from u:
v
x
y
w
z
(u,v)
(u,x)
(u,x)
(u,x)
(u,x)
destination
link
resulting forwarding table in u:

## Slide 84: Dijkstra’s algorithm, discussion
algorithm complexity: n nodes
each iteration: need to check all nodes, w, not in N
n(n+1)/2 comparisons: O(n2)
more efficient implementations possible: O(nlogn)
oscillations possible:
e.g., support link cost equals amount of carried traffic:
A
D
C
B
1
1+e
e
0
e
1
1
0
0
initially
A
D
C
B
given these costs,
find new routing….
resulting in new costs
2+e
0
0
0
1+e
1
A
D
C
B
given these costs,
find new routing….
resulting in new costs
0
2+e
1+e
1
0
0
A
D
C
B
given these costs,
find new routing….
resulting in new costs
2+e
0
0
0
1+e
1